## Slide 1: FPGA-Accelerated Simulation Technologies (FAST)
Derek Chiou
University of Texas at Austin
Electrical and Computer Engineering

## Slide 2: An Early Picture
December 2005, Berkeley

## Slide 3: RAMP Project Timeline
2006
2007
2008
2009
2010
RAMP-Blue
Protoflex
FAST
HAsim
Wavescalar
Purple
RAMP-Red
RAMP-White
RAMP-Gold
Prototypes
Simulators
Wash
Texas
Stanford
Intel/MIT
CMU
Prototype: Implement target system in FPGAs
  Every register/gate in target is in prototype
  Port ASIC RTL to FPGAs or develop RTL for FPGAs
Time scaled prototype
  Delay transactions to adjust relative times
    E.g., delay memory requests/replies to model slower memory
Simulator: Implement model of target in FPGAs
  Not every target register/gate
  May be very different than target
    Split functional/timing
    Analytical model
  But predicts the performance of target, executes code
2005

## Slide 4: My First RAMP Retreat talk: Confessions of a RAMP Heretic
Most Pre-RAMP efforts were prototypes
Initial RAMP thrust was time scaled prototype
FAST has always been a simulator, not a prototype
  Wanted to be able to simulate complex target ISAs, micro-architectures, single threaded but also lots of cores, REAL SOFTWARE
    Use real ISA as baseline to avoid non-research software infrastructure
  Tradeoff simulation performance for accuracy
  Perfect (RTL-level) accuracy
Question: how fast can simulators of computers run?
  Must be parallelized
  Must include hardware
How can simulators be efficiently accelerated by hardware at
  Reasonable (approach software simulator) effort
  Reasonable hardware
RAMP-White was to be a host platform on which to run FAST

## Slide 5: Sim Parallelization: How To Partition and How to Map?
Paritioning on target module boundaries requires balanced speed of each simulation component, fast, balanced communication
Either purely
  software (slow)
  hardware (hard)
Is a hybrid hardware/software possible?
Rename
RS
Br
ALU
Decode
Fetch
dTLB
L2
L1
iTLB
L1
ROB
Rename
RS
Br
ALU
Decode
Fetch
dTLB
L2
L1
iTLB
L1
ROB
Memor
y
Host 0
CPU
Host 1
CPU
Host 2
CPU
Host
FPGA

## Slide 6: Functional/Timing Partitioned
Functional model could be
  Pure software (QEMU, Bochs, Simics, SimNow)
    Many optimization techniques (e.g., just-in-time compilation)
    No better hardware for executing ISA than processor
    Makes adding instructions trivial
  Pure Hardware (Hoe et al)
  Hybrid (Hoe et al)
Timing model is simplified, can be easily implemented in hardware
Functional
Model
(ISA)
Timing
Model
(Micro-architecture)
Inst stream
FPGA
Full-System
Simulator

## Slide 7: Such Partitioning is Normally Tightly Coupled for Accuracy
Fetch
Decode
Execute
Memory
Writeback
Perform
Fetch
Src/dest regs
Opcode
virtual/physical address
Dest reg
Functional Information
Timing
Model
Renaming
Delay based on opcode
Model loads/stores, $
Free register. Could pass from decode
If Functional Information target correct, can model timing perfectly
Traditional accurate simulators (TD) have TM trigger FM to execute
in target correct order: requires tight coupling of FM and TM
Fetch
Decode
Execute
Memory
Writeback
BP
Functional
Model

## Slide 8: FAST: Functional Model Speculatively Executes, First Generates Trace
Fetch
Decode
Execute
Memory
Writeback
IP
Src/dest regs
Opcode
virtual/physical address
Dest reg
Functional Information
Timing
Model
Renaming
Delay based on opcode
Model loads/stores, $
Free register. Could pass from decode
Func
Model
(ISA)
However, functional information is incorrect
BP

## Slide 9: FAST: Wrong Path (Branch Misprediction) Instructions
Fetch
Decode
Execute
Memory
Writeback
M[R1]=R0
R0=R0+1
BRz L1
R0=M[R1]
-----
Functional Information
Timing
Model
Renaming
Delay based on opcode
Model loads/stores, $
Free register. Could pass from decode
R0=M[R1]
BRz L1
R0=R0+1
L1: M[R1]=R0
BP

## Slide 10: FAST: Wrong Path (Branch Misprediction) Instructions
11: BRz 13
Fetch
Decode
Execute
Memory
Writeback
12: R0=R0+1
11: BRz 13
10: R0=M[R1]
-----
-----
Functional Information
Timing
Model
Renaming
Delay based on opcode
Model loads/stores, $
Free register. Could pass from decode
10: R0=M[R1]
11: BRz 13
12: R0=R0+1
13: M[R1]=R0
13
13: M[R1]=R0
What if BP mis-predicted? Timing dependent

## Slide 11: FAST: Memory Reorderings
Fetch
Decode
Execute
Memory, Value = 0
Writeback
----
M[20]=0
BRz L1
R0=M[20]
Value=1
-----
Functional Information
Timing
Model
Renaming
Delay based on opcode
Model loads/stores, $
Free register. Could pass from decode
R0=M[R1]
BRn L1
R0=R0+1
L1: M[R1]=R0
BP
Value-based (not order based) technique for arbitrary
memory models, data speculation, faults, branch misprediction

## Slide 12: FAST Technique: Speculative Functional First
Oracles enables functional model executing first to be accurate
  Target Memory Oracle (TMO)
    Functional store values passed in trace
    By the time stores executed by TM, values have been corrected to being target correct
  Branch predictor
SFF enables independent optimization of FM/TM
  FM has no micro-architectural knowledge
    E.g., no need for register renaming
    Can be implemented in software using best software functional techniques
    Can be aggressively parallelized with no loss in accuracy
    Can be implemented in hardware by providing trace/correction!
  FM provides full functionality (no need to transplant)
  TM can be far away, highly optimized for its tasks
    Does not do any functionality (though oracles need to be maintained)

## Slide 13: FAST Prototype Overview
Software (QEMU modified with trace/rollback) functional model
  Eventually hardware functional model, but software sim exists
FPGA-based timing model written in Bluespec
  Complex OoO micro-architecture fits in a single FPGA
  Multiple host cycles
trace
Functional
Model
Software
Timing
Model
Bluespec HDL
Processor
FPGA
DRC
Computer
HT
Xilinx FPGA
PowerPC 405
Xilinx/Intel
ACP
FSB

## Slide 14: FAST 2007 on DRC in Real Time (~1.2MIPS)

## Slide 15: Current Status
Fully parallelized QEMU functional model
  Trace, accumulating correction
  85%-90% parallel efficiency
~25MIPS with all features on single host core
  Target flexibility
    Single core target
    Multicore target
  100MIPS with a 4/6 core host processor + FPGA
  ~35MIPS/host core with just trace
FPGA platform reliability issues
  Starting port to ML605/XUP

## Slide 16: SFF FM On Single Host Core Versus Full Simulators
Chart: 
| OOO | OOO | OOO | OOO | OOO | OOO | OOO | OOO | GEMS | Intel | M5 | PTL | SESC | SFF | sim-mase | Zesto
Max of MIPS | 0.025 | 0.005 | 0.013 | 0.35 | 1 | 40 | 1.21 | 0.139
Max of Ratio | 5 | 1 | 2.6 | 70 | 200 | 8000 | 242 | 27.8

## Slide 17: Future of FAST
FAST is continuing at full speed
  Dealing with FPGA platform issues
Full system, RTL-level accurate capable, x86 simulator to 4096 cores
Power modeling with Freescale
  6% RMS cycle-by-cycle models for Freescale superscalar out-of-order core, ARM A8 (dual issue in-order)
Fault modeling with Intel
FAST2Imp with AMD
  Defining better decomposition of processors, memory, network
  Will lead to easier to write timing models, better simulators/implementations
Joint research with software academic, will provide highly scalable platform
  Pingali (UT), Brooks (Harvard), Sarkar (Rice)
Our own architectural and micro-architectural ideas
NIFD (GDB front end for FPGAs, see Hari for demo)
FAbRIC-based or FAbRIC-like distribution

## Slide 18: Big Thanks to
Xilinx for funding/FPGAs
NSF/DOE/SRC for funding
Intel/IBM/Freescale/AMD for funding, equipment, and collaboration
Students (who did all the work)
  Hari Angepat, Nikhil A. Patil, Dam Sunwoo
  Joonsoo Kim, Ram Chakravarthy Gene Wu, Yi Yuan
  And several others