## Slide 1: RAMP Gold Wrap
Krste Asanovic
RAMP Wrap
Stanford, CA
August 25, 2010

## Slide 2: RAMP Gold Team
Graduate Students
Zhangxi Tan
Andrew Waterman
Rimas Avizienis
Yunsup Lee
Henry Cook
Sarah Bird
Faculty
Krste Asanovic
David Patterson

## Slide 3: Multicore Architecture Simulation Challenge
Bigger, more complex target system
  Many cores, more components, cache coherence, …
  Need to run OS scheduler, or multithreaded run time
Sequential software simulator performance no longer scaling
  More cores, not faster cores
Detailed software simulators don’t parallelize well
  Cycle-by-cycle synchronization kills parallel performance
Parallel code has non-deterministic performance
  Need multiple runs to get error bars
Software more dynamic, adaptive, autotuned, JIT, …
  Can’t use sampling
~No legacy parallel software
  Need to write/port entire stack.

## Slide 4: RAMP Blue, July 2007
1,008 modified MicroBlaze cores
FPU (64-bit)
RTL directly mapped to FPGA
90MHz
Runs UPC version of NAS parallel benchmarks.
Message-passing cluster
No MMU
Requires lots of hardware
  21 BEE2 boards / 84 FPGAs
Difficult to modify
FPGA computer, not a simulator!

## Slide 5: Dimensions in FAME (FPGA Architecture Model Execution)
  Direct: One target cycle executed in one FPGA host cycle
  Decoupled: One target cycle takes one or more FPGA cycles
  Full RTL: Complete RTL of target machine modeled
  Abstract RTL: Partial/simplified RTL, split functional/timing
  Host single-threaded: One target model per host pipeline
  Host multi-threaded: Multiple target models per host pipeline

## Slide 6: Host Multithreading
CPU1
CPU2
CPU3
CPU4
Target Model
Multithreading emulation engine reduces FPGA resource use and improves emulator throughput
Hides emulation latencies (e.g., communicating across FPGAs)
Multithreaded Emulation Engine (on FPGA)
+1
2
PC
1
PC
1
PC
1
PC
1
I$
IR
GPR
GPR
GPR
GPR
X
Y
2
D$
Single hardware pipeline with multiple copies of CPU state

## Slide 7: RAMP Gold, November 2009
Rapid accurate simulation of manycore architectural ideas using FPGAs
Initial version models 64 cores of SPARC v8 with shared memory system on $750 board
Hardware FPU, MMU, boots OS.
 | Cost | Performance (MIPS) | Simulations per day
Simics Software Simulator | $2,000 | 0.1 - 1 | 1
RAMP Gold | $2,000 + $750 | 50 - 100 | 100
7

## Slide 8: RAMP Gold Target Machine
SPARC V8
CORE
I$
D$
DRAM
Shared L2$ / Interconnect
SPARC V8
CORE
I$
D$
SPARC V8
CORE
I$
D$
SPARC V8
CORE
I$
D$
…
64 cores
8

## Slide 9: RAMP Gold Model
Functional Model Pipeline
Arch State
Timing Model Pipeline
Timing State
RAMP emulation model for Parlab manycore
SPARC v8 ISA
Single-socket manycore target
    Split functional/timing model, both in hardware
      Functional model: Executes ISA
      Timing model: Capture pipeline timing detail (can be cycle accurate)
    Host multithreading of both functional and timing models
    Built for Virtex-5 systems (ML505 or BEE3)
9

## Slide 10: Case Study: Manycore OS Resource Allocation
Spatial resource allocation in a manycore system is hard
  Combinatorial explosion in number of apps and number of resources
Idea: use predictive models of app performance to make it easier on OS
HW partitioning for performance isolation (so models still work when apps run together)
Problem: evaluating effectiveness of resulting scheduling decisions requires running hundreds of schedules for billions of cycles each
Simulation-bound: 8.3 CPU-years for Simics!
Read ISCA’10 FAME paper for details

## Slide 11: Case Study: Manycore OS Resource Allocation
Chart: Normalized Runtime
| Synthetic Only | PARSEC Small
worst sched. | 1.5968 | 2.1774
chosen sched. | 1.0121 | 1.2391
best sched. | 1 | 1

## Slide 12: Case Study: Manycore OS Resource Allocation
The technique appears to perform very well for synthetic or reduced-input workloads, but is lackluster in reality!
Chart: Normalized Runtime
| Synthetic Only | PARSEC Small | PARSEC Large
worst sched. | 1.5968 | 2.1774 | 3.847
chosen sched. | 1.0121 | 1.2391 | 1.7159
best sched. | 1 | 1 | 1

## Slide 13: RAMP Gold Distribution
http://sites.google.com/site/rampgold/
BSD/GNU licenses
Many (100?) downloads
Used by Xilinx tools group as exemplar System Verilog design

## Slide 14: RAMP Gold Lessons
Architects will use it!
  Actually, don’t want to use software simulators now
Make everything a run-time parameter
  Avoid resynth + P&R
Difficult to modify highly tuned FPGA designs
Functional/Timing split should be at µarch. block level
  Really build a microfunctional model
Standard ISA only gets you so far in research
  Research immediately changes ISA/ABI, so lose compatibility
Target machine design vital part of architecture research
  Have to understand target to build a model of it!
  Need area/cycle-time/energy numbers from VLSI design
FAME-7 simulators are very complex hardware designs
  Much more complicated than a processor

## Slide 15: Midas Goals
Richer set of target machines
  In-order scalar cores, possibly threaded, + various kinds of vector unit
  Various hardware-managed plus software-managed memory hierarchies
  Cross-chip and off-chip interconnect structures
More modular design
  Trade some FPGA performance to make modifications easier
Better/more timing models
  Especially interconnect and memory hierarchy
Better I/O for target system
  Timed I/O to model real-time I/O accurately
  Paravirtual-style network/video/graphics/audio/haptic I/O devices
Better scaling of simulation performance
  Weak scaling – more FPGA pipelines allow bigger system to run faster
  Strong scaling – more FPGA pipelines allow same system to run faster
First target machine running apps on Par Lab stack in 2010

## Slide 16: Midas ISA Choice
RISC-V: A new home-grown RISC ISA
  V for Five, V for Vector, V for Variants
  Inspired by MIPS but much cleaner
  Supports 32-bit or 64-bit address space
  32-bit instruction format plus optional variable length (16/32/>32)
  Designed to support easy extension
  Completely open (BSD)
Are we crazy not to use a standard ISA?
  Standard ISA not very helpful, but standard ABI is
  Standard ABI effectively means running same OS
  Running same OS means modeling hardware platform – too much work for university
  Also, only interesting standard ISAs are x86 & ARM (+GPU), both are too complex for university project to implement in full
  We’re going to change ISA plus OS model anyway
  Midas modularity should make it easy to add other ISAs as well

## Slide 17: Midas Target Core Design Space
Scalar cores
  In-order (out-of-order possible later)
  Different issue widths, functional-unit latencies
  Decoupled memory system (non-blocking cache)
  Optional multithreading
  New translation/protection structures for OS support
  Performance counters
Attached data-parallel accelerator options
  Traditional vector (a la Cray)
  SIMD (a la SSE/AVX)
  SIMT (a la NVIDIA GPU)
  Vector-threading (a la Scale/Maven)
  All with one or more lanes
Should be possible to model mix of cores for asymmetric platforms (Same ISA, different µarchitecture)

## Slide 18: Midas Uncore Design Space
Distributed coherent caches
  Initially, using reverse-map tag directory
  Flexible placement, replication, migration, eviction policies
Virtual local stores
  Software-managed with DMA engines
Multistage cross-chip interconnect
  Rings/torus
Partitioning/QoS hardware
  Cache capacity
  On-chip and off-chip bandwidth
DRAM access schedulers
Performance counters
All fully parameterized for latency/bandwidth settings

## Slide 19: Platforms of Interest
1W – handheld
10W – laptop/settop/TV/games/car
100W – servers

## Slide 20: Midas Software
Gcc+binutils as efficiency-level compiler tools
  Already up and running for draft RISC-V spec
Par Lab OS + software stack for the rest
Par Lab applications
Pattern-specific compilers build with SEJITS/Autotuning help get good app performance quickly on large set of new architectures

## Slide 21: Not just simulators
New DoE-funded Project Isis (with John Wawrzynek) on developing high-level hardware design capability
Integrated approach spanning VLSI design and simulation
Building ASIC designs for various scalar+vector cores
  Yes, we will fab chips
Mapping RTL to FPGAs
  FPGA computers help software developers, helps debug RTL
Why #1. For designing (not characterising) simple cores, power model abstractions don’t work (e.g., 2x difference based on data values).

## Slide 22: Acknowledgements
Sponsors
  ParLab: Intel, Microsoft, UC Discovery, National Instruments, NEC, Nokia, NVIDIA, Samsung, Sun Microsystems
  Xilinx, IBM, SPARC International
  DARPA, NSF, DoE, GSRC, BWRC