## Slide 1: Using FPGAs for Systems Research Successes, Failures, and Lessons
Jared Casper, Michael Dalton, Sungpack Hong, Hari Kannan, Nju Njoroge, Tayo Oguntebi, Sewook Wee, Kunle Olukotun,
Christos Kozyrakis
Stanford University
Talk at RAMP Wrap Event – August 2010

## Slide 2: Use of FPGAs at Stanford
A mean to continue Stanford’s systems tradition
  MIPS, MIPS-X, DASH, FLASH, …
Four main efforts from 2004 till today
  ATLAS: a CMP with hardware for transactional memory
  FARM: a flexible platform for prototyping accelerators
  Raksha: architectural support for software security
  Smart Memories: verification of a configurable CMP
    See talk by M. Horowitz tomorrow

## Slide 3: Common Goals
Provide fast platforms for software development
  What can apps/OS do with new hardware features?
  Have the HW platform early in the project
Fast iterations between HW and SW
Capture primary performance issues
  E.g., scaling trends, bandwidth limitations,…
Expose HW implementation challenges
Not a goal: accurate simulation of a target uarch

## Slide 4: ATLAS (aka RAMP-Red)
Goal: a fast emulator of the TCC architecture
  TCC: hardware support for transactional memory
  Caches track read/write sets; bus enforces atomicity
  What does this mean for system and for software?
Main Memory & I/O
Coherent Bus with TM Support
CPU0
Cache +TM
CPU1
Cache +TM
CPU2
Cache +TM
CPU7
Cache +TM
…

## Slide 5: ATLAS on the BEE2 Board
PPC 0
+ TM
PPC 1
+ TM
I/O
Linux PPC
PPC 2
+ TM
PPC 3
+ TM
PPC 4
+ TM
PPC 5
+ TM
PPC 7
+ TM
PPC 8
+ TM
Control Switch
DRAM
User Switch
User Switch
User Switch
User Switch
9-way CMP system at 100MHz
  Use hardwired PPC cores but synthesized caches
  Uniform memory architecture
  Full Linux 2.6 environment

## Slide 6: ATLAS Successes
1st hardware TM system
100x faster than our simulator
  Close match in scaling trend & TM bottleneck analysis
Ran high-level application code
  Targeted by our OpenTM framework (OpenMP+TM)
Research using ATLAS
  A partitioned OS from CMPs with TM support
  A practical tool for TM performance debugging
  Deterministic replay using TM
  Automatic detection for atomicity violations

## Slide 7: ATLAS Successes (cont)
Hands-on tutorials at ISCA’06 & ASPLOS’08
  >60 participants from industry & academic
  Wrote, debugged, and tuned parallel apps on ATLAS
    From sequential to ideal speedup in minutes

## Slide 8: ATLAS Failures
Limited interest by software researchers
  Still too slow compared to commercial systems (latency)
    9 PPC cores at 100MHz slower than a single Xeon core
    We are competing with Xeons & Opterons, not just simulators!!
    Large-scale will be the key answer here
  Small number of boards available (bandwidth)
    The need for cheap platforms
  Software availability for (embedded) PowerPC cores
    Java, databases, etc

## Slide 9: Lessons from ATLAS
Software researchers need fast base CPU & rich SW environment
Pick FPGA board with large user community
Tools/IP compatibility and maturity are crucial
IP modules should have good debugging interfaces
Designs that cross board boundaries are difficult
FPGAs as a research tool
  Adding debugging/profiling/etc features is straightforward
  Changing the underlying architecture can be very difficult

## Slide 10: FARM: Flexible Architecture Research Machine
Goal: fix the primary issue with ATLAS
  Fast base CPU & rich software environment
FARM features
  Use systems with FPGAs on coherence fabric
    Commodity full-speed CPUs, memory, I/O
    Rich SW support (OS, compilers, debugger … )
    Real applications and real input data
  Tradeoff: cannot change the CPU chip or bus protocol
    But can work on closely coupled accelerators for compute (e.g., new cores), memory, and I/O
    Can put a new computer in the FPGA as well

## Slide 11: FARM Hardware Vision
CPU + GPU for base computing
FPGAs add the flexibility
Extensible to multiboard
  Through high-speed network
Many emerging boards that match the description
  DRC, XtremeData, Xilinx/Intel, ACP, A&D Procyon
Memory
Memory
Memory
Memory
Core 0
Core 1
Core 2
Core 3
Core 0
Core 1
Core 2
Core 3
FPGA
SRAM
GPU / Stream
IO

## Slide 12: The Procyon Board by A&D Tech
Initial platform for single FARM node
CPU Unit (x2)
  AMD Opteron Socket F (Barcelona)
  DDR2 DIMMs x 2
FPGA Unit (x1)
  Stratix II, SRAM, DDR, debug
Units are boards on cHT backplane
  Coherent HyperTransport (version 2)
  Implemented cHT compatibility for FPGA unit

## Slide 13: Inside FARM
Interfaces to user application
  Coherent caches, streaming, memory-mapped registers
  Write buffers, prefetching, epochs for ordering, …
Verification environment
2MB
L3 Shared Cache
…
Hyper
Transport
2MB
L3 Shared Cache
Hyper
Transport
32 Gbps
32 Gbps
~60ns
AMD Barcelona
6.4 Gbps
~380ns
6.4 Gbps
cHTCore™
Hyper Transport (PHY, LINK)‏
Altera Stratix II FPGA (132k Logic Gates)‏
Configurable
Coherent Cache
Data
Transfer Engine
Cache IF
Data Stream IF
User Application
MMR
IF
1.8G
Core 0
64K L1
512KB
L2 Cache
1.8G
Core 3
64K L1
512KB
L2 Cache
…
1.8G
Core 0
64K L1
512KB
L2 Cache
1.8G
Core 3
64K L1
512KB
L2 Cache
*cHTCore by the University of Manhiem

## Slide 14: FARM Successes (so far)
Up and running
  Coherent interface, OS modules, user libs, verification, …
TMACC: an off-core TM accelerator
  Hardware TM support without changing cores/caches
  Large performance gains for coarse-grain transactions
    The important case for TM research
    Over STM or threaded core running on Opterons
  Showcases simpler deployment approaches for TM
Ongoing work on heterogeneous accelerators
  For compute, memory, I/O, programmability, security, …

## Slide 15: FARM Failures
Too early to say…

## Slide 16: Lessons from FARM (so far)
CPU+FPGA boards are promising but not mature yet
  Availability, stability, docs, integration, features, …
  We had several false starts: DRC, XtremeData
  Forward compatibility of infrastructure is still an unknown
Vendor support and openness is crucial
  Faced long delays and roadblocks in many cases
  This is what made the difference with A&D Tech
Cores & systems not yet optimized for coherent accelerators
  Most work goes into CPU/FPGA interaction (HW and SW)
  Will likely change thanks to CPU/GPU fusion and I/O virtualization

## Slide 17: Raksha: Architectural Support for Software Security
Goal: develop & realistically evaluate HW security features
  Avoid pitfalls of separate methodologies for functionality and performance
  Primarily focused on dynamic information flow tracking (DIFT)
Primary prototyping requirements
  A baseline core we could easily change
    Simple core, mature design, reasonable support
  Rich software base (Linux, libraries, software)
    SW modules and security policies a critical part of our work
    Also needed for credible evaluation
  Low cost FPGA system

## Slide 18: Raksha: 1st Generation
Base: Leon Sparc V8 core + Xilinx XUP board
  Met all our critical requirements
Changes to the Leon design
  New op mode, multi-bit tags on state, check & propagate logic, …
Security checks on user code and unmodified Linux
  No false positives
Policy Decode
Tag ALU
Tag Check
PC
Decode
D-Cache
RegFile
ALU
I-Cache
Traps
WB
Notes: 1 slide on pipeline
- state extended by tags
- tag ops in parallel with data ops (same forwarding etc)
1 slide on multigranularity tags through software
- machine supports world-level tags
- coarse-grain to lower the overhead (see Suh’s paper)
- byte or bit level using software handler to maintain metadata on the side (say about ok if uncommon)

## Slide 19: Raksha: 2nd Generation
Repositioned hardware support to a small coprocessor
  Motivated by industry feedback after using prototype
    Complex pipelines are difficult to change/verify
  No changes to the main core; reusable coprocessor; minor performance overhead
Processor
Core
I Cache
D Cache
ROB
Policy Decode
Tag ALU
Tag Check
Tag Cache
Tag RF
W B
DIFT Coprocessor
PC, Inst, Address
Security exception
L2 Cache
Notes: 1 slide on pipeline
- state extended by tags
- tag ops in parallel with data ops (same forwarding etc)
1 slide on multigranularity tags through software
- machine supports world-level tags
- coarse-grain to lower the overhead (see Suh’s paper)
- byte or bit level using software handler to maintain metadata on the side (say about ok if uncommon)

## Slide 20: Raksha: 3rd Generation (Loki)
Collaboration with David Mazieres’ security group
Loki: HW support for information flow control
  Tags encode SW labels for access rights; enforced by HW
Loki + HiStar OS: enforce app security policies with 5KLOC of trusted OS code
  HW can enforce policies even if rest of OS is compromised
Permission
Checks
Decode
D-Cache
RegFile
ALU
I-Cache
Traps
WB
Execute
P-Cache
Read/Write
P-Cache
Notes: 1 slide on pipeline
- state extended by tags
- tag ops in parallel with data ops (same forwarding etc)
1 slide on multigranularity tags through software
- machine supports world-level tags
- coarse-grain to lower the overhead (see Suh’s paper)
- byte or bit level using software handler to maintain metadata on the side (say about ok if uncommon)

## Slide 21: Raksha Successes
Provided a solid platform for systems research
  All but 2 Raksha papers used FPGA boards
  Including papers focusing on security policies
Showcased the need for HW/SW co-design
  Showed that security policies developed with simulation are flawed!!
Convincing results with lots of software
  Two Oses, LAMP stack, 14k software packages
Fast HW/SW iterations with a small team
  3+ designs by 2 students in 3.5 years
Shared it with 4 other institutes
  Academia and industry

## Slide 22: Raksha Failures
?

## Slide 23: Lessons from Raksha
The importance of a robust base
  Base core(s), FPGA board, debug, CAD tools, …
Keep it simple, stupid
  Just like other tools, a single FPGA-based tool cannot do it all
  Build multiple tools, each with a narrow focus
    Can share across tools under the hood though
  Don’t over-optimize HW; work on SW and system as well
Killer app for RAMP may not be about performance
  Difficult to compete with CPUs/GPUs on performance
  But possible to have other features that attract external users

## Slide 24: Conclusions
FPGA frameworks are playing a role in systems research
We delivered on a significant % of the RAMP vision
  Demonstrated feasibility and advantages
  Research results using FPGA environments
  Understand better the constraints and potential solutions
The road ahead
  Scalability (1,000s of cores), ease-of-use, cost, …
  Focus on frameworks with a narrower focus?
    E.g., accelerators, security, …
    Sharing between frameworks under the hood

## Slide 25: Questions?
More info and papers from there projects at http://csl.stanford.edu/~christos